## Slide 1
FPGA Tick-to-Trade
A simulated high-frequency trading engine on silicon — from price message to order in ~176 nanoseconds, with perfectly fixed latency
9 steps, explained simply | Spec-only, pre-implementation
Source: fpga_tick_to_trade_master_spec.md v2.0 + ml_engineer_brief.md · Target: Artix-7 XC7A35T-2FGG484I @ 125 MHz · Vivado/Vitis HLS 2023.x

## Slide 2
The Project in One Glance
A super-fast simulated trading system on an FPGA chip
No real money, no real exchange — a portfolio demo
Goal: prove you can make trading decisions in ~176 ns with perfectly fixed latency
Verified with 1,000,000+ messages, never dropping or losing one
Every trade checked by a tiny AI before it leaves
1. The Problem — why speed matters
2. The Mail Format — how price messages look
3. The Ears — how the FPGA receives mail
4. The Notebook — tracking top of book
5. The Clues — extracting 8 market hints
6. The AI Brain — predicting a risky trade
7. The Trading Rule — deciding to buy/sell
8. The 9 Security Guards — blocking danger
9. The Exit & Stopwatch — send + prove speed
FPGA Tick-to-Trade Simulator
2

## Slide 3
STEP 1
The Problem — Why Speed Matters
The stock market is a live auction — everyone hears the price at the same second, and the first to shout "I'LL BUY!" gets the deal. One microsecond slow = it's gone.
A normal computer reacts unpredictably: sometimes 2 µs, sometimes 50 µs (it gets slow exactly when the market is most busy).
An FPGA is a fixed assembly line, not a multitasking person — every price message takes the exact same physical path, so time is always identical, e.g. exactly 22 ticks ≈ 176 nanoseconds.
Project goal: build the assembly line that listens, decides, double-checks with AI, and sends a fake order back — all in a fixed, tiny amount of time.
Listen to fake price messages from a laptop
Decide if it's a good time to trade
Double-check with an AI if it's risky
Send a fake order back — and prove no message was ever lost, even over 1,000,000 messages in a row
FPGA Tick-to-Trade Simulator
3

## Slide 4
STEP 2
The Mail Format — The 16-Byte Postcard
Every price update is a standard postcard: exactly 16 bytes, 6 boxes, always in the same place (big-endian / network byte order).
Because the size never changes, the FPGA just counts — it never has to guess where a message ends.
Box | Means | Example
Type (1B) | Kind of news | 0x01 update · 0x02 trade · 0x03 clear · 0xFF heartbeat
Symbol (1B) | Which item | 1 = Apples, 2 = Oranges (watch 4)
Side (1B) | Which side | 0 = BUY, 1 = SELL (trade: aggressor)
Price (4B) | Price in cents | 10001 = $100.01 (integers only)
Qty (4B) | How many | 50 apples · 0 = side empty
Seq # (4B) | Counting 1,2,3… | 1,2,4 ⇒ #3 was lost
  Two tricks
Packing: one Ethernet frame holds 1–88 postcards (88×16 = 1408 bytes), streamed back-to-back
Two envelopes: Mode 0 raw Ethernet (0x88B5) = training wheels; Mode 1 real UDP/IPv4 (port 60000) = the real road
Reply postcard is also 16 bytes: Type 0x10/0x11/0x12, symbol, side, reject reason, price, qty, trigger_seq, latency_cyc
LINK_MODE selects the envelope — the assembly line doesn't care
FPGA Tick-to-Trade Simulator
4

## Slide 5
STEP 3
The Ears — How the FPGA Receives Mail
Station | Module | Job
A | rgmii_to_gmii | Translator: 4-lane dual-sided highway (RGMII DDR @125 MHz) → orderly 1-byte-per-tick belt
B | eth_mac_rx | Mailroom: strips preamble/SFD, verifies FCS; damaged envelopes trashed + counted (err_fcs)
C | frame_classifier | Guard: Mode 0 → EtherType 0x88B5; Mode 1 → IPv4 + IHL=5 + checksum + UDP port 60000; per-reason counters
D | md_parser | Opener: cuts payload into exact 16-byte postcards; length not divisible by 16 → trash (err_frame_len)
At the very last byte entering Station D, we stamp the time — that is the "start" of the latency stopwatch, carried with the message.
Everything up to here is about getting mail cleanly without dropping anything, at minimum inter-frame gap for 10,000 frames.
FPGA Tick-to-Trade Simulator
5

## Slide 6
STEP 4
The Notebook — Tracking Top of Book
A tiny notebook with 4 pages (NUM_SYMBOLS=4): Apples, Oranges, Bananas, Grapes
Each page holds only the top of book: best BUY (bid) price+qty and best SELL (ask) price+qty, each with a valid bit
Spread = ask − bid · Mid = (bid+ask) >> 1
Book starts invalid on reset; crossed (bid ≥ ask, both valid) flags cnt_crossed and later guards block trading
Station | Module | Job
E | symbol_filter | Bouncer: 4-entry CAM picks only our symbols; else discard + cnt_filtered
F | seq_monitor | Missed-mail detector: gap → sticky seq_gap + stale (block until resync); duplicate → drop; 10 ms staleness timer
G | tob_engine | Notebook keeper: 1-cycle replace per side; qty=0 clears valid; 0x03 clears book; 0x02/0xFF don't touch book
All later steps read from this notebook.
FPGA Tick-to-Trade Simulator
6

## Slide 7
STEP 5
The Clues — 8 Market Hints (Features)
Clue | Name | Formula | Plain English
F0 | Spread | a_t − b_t | Is the buyer/seller gap wide or narrow?
F1 | Mid delta | m_t − m_(t−1) | Did the middle price move up/down?
F2 | Book imbalance | q_b − q_a | More buyers or more sellers?
F3 | Bid-size change | q_b,t − q_b,t−1 | Did buyers grow/shrink?
F4 | Ask-size change | q_a,t − q_a,t−1 | Did sellers grow/shrink?
F5 | Update rate | updates in last W events | How busy is the market? (W=16)
F6 | Last trade side | buy +1 / sell −1 / none 0 | Who started the last trade?
F7 | Volatility proxy | Σ¦mid deltas¦ (last W) | How much did price jitter?
Computed after every book update in 1 tick — add/subtract/shift/compare only
Wide spread = low interest; narrow = crowded, active market
Squeezer (feature_normalizer) maps raw clues to int8 −128..127 via offset + arithmetic shift, saturating not wrapping
Result: 8 tiny numbers — the exact AI input
FPGA Tick-to-Trade Simulator
7

## Slide 8
STEP 6
The AI Brain — Predicting a Risky Trade
A tiny AI that answers ONE question: "if we quote now, will the price move against us and we get adversely selected?"
Adverse selection = you sell at $10, price crashes to $8, you're stuck
Score: z = b + w0·x0 + w1·x1 + … + w7·x7
8 weights learned in training; int32 exact, no silent truncation
It does NOT buy or sell — it only vetoes
Hysteresis (two lines, no flicker) z ≥ T_high → Risky = 1 (block) z ≤ T_low → Safe = 0 (allow) in between → hold previous
Fail-safe (FR-31): invalid / crossed / gap / stale data ⇒ adverse_risk forced to 1 — better to block than trade on garbage.
Runs in parallel with the trading rule — the rule's order intent is delayed through a fixed-depth [ALIGN] shift register so both arrive at the risk engine the same cycle, every cycle (NFR-14).
FPGA Tick-to-Trade Simulator
8

## Slide 9
STEP 7
The Trading Rule — Deciding to Buy or Sell
A simple, fixed, deterministic rule — not AI. The AI only vetoes.
Wakes up after every book-modifying update and asks: should we trade?
Cheap math only: barrel-shift, compare, subtract — no DSP on signal path
Takes just 1 tick; intent delayed via [ALIGN] to meet the AI verdict at the same cycle
BUY (FR-35): buy order iff • both sides valid, not crossed • spread ≥ cfg_min_spread (2 ticks) • bid_qty > ask_qty << 1 (way more buyers) → Buy cfg_order_qty (100) at ask_price
SELL (FR-36): mirror image • both sides valid, not crossed • spread ≥ cfg_min_spread • ask_qty > bid_qty << 1 (way more sellers) → Sell cfg_order_qty at bid_price
Both true at once is impossible by construction — if ever detected, no order + err_signal_conflict (FR-37).
FPGA Tick-to-Trade Simulator
9

## Slide 10
STEP 8
The 9 Security Guards — Blocking Dangerous Orders
Gate | Blocks if…
0x01 Kill Switch | Operator halt latched — overrides everything (CSR clear to resume)
0x02 Max Size | order_qty > 500 (no fat-finger)
0x03 Max Position | ¦position ± qty¦ > 1000 exposure bound
0x04 Price Band | ¦order price − mid¦ > 50 ticks (corrupt price)
0x05 Stale Data | no update for 10 ms
0x06 Sequence Gap | sticky seq_gap — book unreliable until resync
0x07 Crossed/Locked | bid ≥ ask both valid — physically impossible
0x08 Throttle | token bucket empty (8 tokens, 100 µs refill)
0x09 Adverse Selection (ML) | adverse_risk = 1 → block, or reduce size (cfg_ml_action)
All 9 check in parallel in a single cycle (FR-42) — any raised hand blocks
No path bypasses the risk engine (FR-41)
Every block increments that guard's counter
If 2 fire at once: both counted, reject_reason = lowest-numbered gate (hard gates 0x01–0x08 dominate ML 0x09)
ML 0x09 is advisory — never overrides hard gates
All 9 pass ⇒ intent becomes a real order
FPGA Tick-to-Trade Simulator
10

## Slide 11
STEP 9
The Exit — Sending the Order
order_builder + eth_mac_tx encode the order with correct framing for the active LINK_MODE (incl. IPv4 checksum in Mode 1)
~1 tick from risk pass → first order byte; frame occupies TX ~84 cycles
Settings via CSR map — effect applies at next message boundary
Tracks lat_min / lat_max / lat_last
2-deep output register, NOT a FIFO • 3rd order while 2 pending → dropped, cnt_order_overflow++ • Dropping is correct: a queued stale order trades on outdated info • An unbounded queue would make latency history-dependent, violating NFR-1 (fixed constant latency)
Orders are never reordered relative to their triggering messages; market data arriving during TX is still parsed and applied.
FPGA Tick-to-Trade Simulator
11

## Slide 12
STEP 9
The Stopwatch — Proving the Speed
Free-running 32-bit counter @125 MHz (8 ns period)
Timestamp IN: last byte of message at parser
Timestamp OUT: first byte handed to MAC TX
latency = OUT − IN → 64-bucket BRAM histogram + min/max/last
Emitting latency inside the order = host capture doubles as a latency log
Stage | Cycles
Parser ingress → structured message | 1
Symbol filter (CAM) | 1
Book update (register write) | 1
Feature extraction F0–F7 | 1
Feature normalization | 1
ML classifier (parallel MAC) | 2–3
ML policy (hysteresis) | 1
Risk: all 9 gates incl. ML | 1
Order builder → first byte | 1
Engine total (tick-to-trade) | ~10–11, target ≤22 (176 ns)
Success = histogram shows EXACTLY ONE occupied bucket over the full 1M-message soak (NFR-1/2). A second bucket is a functional bug, not a performance result.
Slow path (CSR, stats, debug UART, histogram) never backpressures the fast path. Single 125 MHz domain; CDC confined to slow path with two-flop synchronizers.
FPGA Tick-to-Trade Simulator
12

## Slide 13
Success Criteria — Project Succeeds If…
1. Back-to-back messages at Gigabit line rate, no drop/reorder, ≥ 1,000,000 messages
2. Tick-to-trade latency fixed — single histogram bucket, max == min
3. Every risk gate incl. ML 0x09 individually demonstrated blocking/reducing, counter per reason
4. Full RTL output matches Python golden models bit-exactly on randomized soak
5. hls4ml IP score z matches Python fixed-point golden bit-exactly on every regression vector
6. Timing met @125 MHz on XC7A35T (WNS > 0); ≤15% LUTs, ≤10% FFs, ≤8 BRAM, 0 DSP (excl. ML ≤8)
7. One-command reproduce: clone repo → run one command → same simulation results
FPGA Tick-to-Trade Simulator
13

## Slide 14
References & Setup
Sources
fpga_tick_to_trade_master_spec.md v2.0 — single source of truth
ml_engineer_brief.md — ML owner handoff (Python/hls4ml only, zero Verilog)
fpga_top_of_book_engine_spec.md — superseded historical document
Target
Artix-7 XC7A35T-2FGG484I, 125 MHz single clock domain
Vivado 2023.x + Vitis HLS 2023.x
Hard rules
Hand-written RTL is Verilog-2001 only (exception: hls4ml/Vitis IP)
ML teammate trains in Python (Keras/TF, hls4ml, ap_fixed<8,8> int8), verifies hls_model.predict() == ml_golden.py bit-exactly before hand-off
Spec-only, pre-implementation — no rtl/ or sim/ yet
FPGA Tick-to-Trade Simulator
14